## Slide 1: CAN Bus Firewall

## Slide 2
Purpose
Ensure compromised IVIs
cannot disrupt
safety critical systems

## Slide 3
Overview
IVI
CAN Firewall
ECU 2
IVI Runs a wide variety of software that may be compromised through telematics link
CAN Firewall Hardware microcontroller on CAN bus filtering CAN traffic based on configurable rules
ECUs Safety-critical vehicle controllers managing breaks, throttle, steering, etc.
ECU 1

## Slide 4
Northbound vs. Southbound Traffic
Receive CAN frame from IVI
Validate CAN frame against rule table
Forward CAN Frame to Vehicle
Southbound traffic
Forward CAN frame to IVI
Validate CAN frame against rule table
Receive CAN Frame from Vehicle
Northbound traffic

## Slide 5
A new firewall rule is created and is signed using device-specific key
Rule is pushed over the air to the IVI
IVI Firewall Manager forwards the signed rule to the firewall as a specific CAN frame
Firewall validates signature of received frame and stores new rule.
Use Case: Update rules
Firewall Manager
IVI
Backend Server
Rule Admin
Firewall
Rule Manager

## Slide 6
Rule Structure [1/2]
Only bits set in the mask will be matched against the filter
Filter
ANDed against the masked Frame ID of incoming frame
Frame IDs passing filter are intercepted
Frame ID of an incoming frame is masked against rule mask
Mask
See http://www.cse.dmu.ac.uk/~eg/tele/CanbusIDandMask.html for details
Mask | Filter | ID XForm | Data XForm | ID Operand | Data Operand
0xFFFFFFFF | 0x00000012 | AND | OR | 0x00FFFFFF | 0x000000FFFFFFFFFF

## Slide 7
Rule Structure [2/2]
Mask | Filter | ID XForm | Data XForm | ID Operand | Data Operand
0xFFFFFFFF | 0x00000012 | AND | OR | 0x00FFFFFF | 0x000000FFFFFFFFFF
ID XForm
Determines transformation applied to outbound Frame ID (SET, AND, OR, XOR, INV)
ID Operand
Transformation operand applied to outbound Frame ID
Data Operand
Transformation operand applied to outbound Data
Data XForm
Determines transformation applied to outbound Data (SET, AND, OR, XOR, INV)
A Rule can also specify that the frame is to be silently dropped or passed as is.

## Slide 8
CAN Rule Table
Prio | Mask | Filter | ID XForm | Data XForm | ID Operand | Data Operand
0x01 | 0xFFFFFFFF | 0x00000012 | AND | OR | 0x00FFFFFF | 0x000000FFFFFFFFFF
0x02 | 0xFFFFFFF0 | 0x00000120 | SET | SET | 0x01234567 | 0x0123456780ABCDEF
0x7E | 0x00000000 | 0x00000000 | DROP | DROP | 0x00000000 | 0x0000000000000000
If no rule matches, the frame is forwarded unmodified to its destination
Prioritize
Rules are applied to incoming frames in order of ascending priority
Match and process
A rule-matching frame is processed by that rule and is then forwarded to its destination
Forward to next rule
A non-matching frame passed on to the rule with the next ascending ID

## Slide 9
CAN Rule Configuration – Common Header
Frame ID | Data: Prio [1] | Data: Cmd [1] | … | …
0x00004711 | 0x04 | [RULE] | … | …
Frame ID [32 bits] Factory-configured CAN Frame that is intercepted and interpreted by the CAN Firewall.
Prio [0x00-0x7F | 0x80-0xFF] [1 byte]
Specifies the priority of the rule that is being prepared and which . 0x00-0x7F applies to northbound traffic. 0x80-0xFF applies to southbound traffic. All commands setting up and storing a single rule will use the same Prio.
Cmd [PREP_RULE1, PREP_RULE2, PREP_RULE3 , PREP_RULE4, PREP_RULE5,PREP_RULE6, STORE_RULE] [1 byte]
Sets up a single rule. PREP_RULE1 – PREP_RULE6 are transmitted with the same Prio. STORE_RULE is then transmitted with the given Prio to store the single rule specified by the previous PREP rule commands.

## Slide 10
CAN Rule Configuration – PREP_RULE1
Frame ID | Prio [1] | Cmd [1] | Mask [4] | XForm [1] | Rsvd [1]
0x00004711 | 0x04 | 0x01 | 0x0000FFFF | 0x01 | 0x00
Cmd [PREP_RULE1] [1 byte]
PREP_RULE1 specifies the rule priority and the mask to apply, and the transform operators for the rule.
XForm [SET_AND] [1 byte] The transformation to apply to Frame ID and Data. Combination of SET, AND, OR, XOR, and NEG. Upper four bits defines Frame ID operator. Lower four bits defines Data operator.
Mask [32 bit value] [4 bytes] Mask to apply to incoming Frame ID prior to filtering.
Reserved for future use. Set to 0

## Slide 11
CAN Rule Configuration – PREP_RULE2
Cmd [PREP_RULE2] [1 byte]
PREP_RULE2 specifies the filter to apply to incoming Frame IDs and the low 16 bits of the Data transformation operand
DtOper1 [16 bit value] [2 bytes] Specifies the lower 16 bits of the data operand to provide to the data transform operator (AND, OR, XOR, NEG).
Filter [4] [32 bit value] [4 bytes] Filter to apply to incoming Frame ID that has been masked.
Frame ID | Prio [1] | Cmd [1] | Filter [4] | DtOper1 [2]
0x00004711 | 0x04 | 0x02 | 0x0000AAC1 | 0x0100

## Slide 12
CAN Rule Configuration – PREP_RULE3
Cmd [PREP_RULE3] [1 byte]
PREP_RULE2 specifies the high 48 bits of the operand to apply to the payload transform operator.
DtOper2 [48 bit value] [6 bytes] Specifies the upper 48 bits of the data operand to provide to the data transform operator (AND, OR, XOR, NEG). DtOper1 and DtOper2 in the example above are concatenated to: 0x0706050403020100
Frame ID | Prio [1] | Cmd [1] | DtOper2 [6]
0x00004711 | 0x04 | 0x03 | 0x070605040302

## Slide 13
CAN Rule Configuration – PREP_RULE4
Cmd [PREP_RULE4] [1 byte]
Specifies the Frame ID operand and the lowest 2 bytes of the HMAC-SHA256 signature
HMAC1 [16 bit value] [2 bytes] Specifies bits 0-15 bits of the HMAC-SHA256 signature, generated with the key flashed into the Firewall at the factory.
IDOper [32 bit value] [4 bytes] Specifies the Frame ID operand to provide to the Frame ID transform operator
Frame ID | Prio [1] | Cmd [1] | IDOper [4] | HMAC1 [2]
0x00004711 | 0x04 | 0x04 | 0xFFFF0000 | 0x0100

## Slide 14
CAN Rule Configuration – PREP_RULE5
Cmd [PREP_RULE5] [1 byte]
Specifies six bytes of the HMAC-SHA256 signature
HMAC2 [48 bit value] [6 bytes] Specifies bits 16-63 of the HMAC-SHA256 signature
Frame ID | Prio [1] | Cmd [1] | HMAC2 [6]
0x00004711 | 0x04 | 0x05 | 0x070605040302

## Slide 15
CAN Rule Configuration – PREP_RULE6
Cmd [PREP_RULE6] [1 byte]
Specifies six bytes of the HMAC-SHA256 signature
HMAC3 [48 bit value] [6 bytes] Specifies bits 64-127 of the HMAC-SHA256 signature
Frame ID | Prio [1] | Cmd [1] | HMAC3 [6]
0x00004711 | 0x04 | 0x06 | 0x0D0C0B0A0908

## Slide 16
CAN Rule Configuration – PREP_RULE7
Cmd [PREP_RULE7] [1 byte]
Specifies six bytes of the HMAC-SHA256 signature
HMAC4 [48 bit value] [6 bytes] Specifies bits 128-175 of the HMAC-SHA256 signature
Frame ID | Prio [1] | Cmd [1] | HMAC4 [6]
0x00004711 | 0x04 | 0x07 | 0x131211100F0E

## Slide 17
CAN Rule Configuration – PREP_RULE8
Cmd [PREP_RULE8] [1 byte]
Specifies six bytes of the HMAC-SHA256 signature
HMAC5 [48 bit value] [6 bytes] Specifies bits 176-223 of the HMAC-SHA256 signature
Frame ID | Prio [1] | Cmd [1] | HMAC5 [6]
0x00004711 | 0x04 | 0x08 | 0x191817161514

## Slide 18
CAN Rule Configuration – PREP_RULE9
Cmd [PREP_RULE9] [1 byte]
Specifies six bytes of the HMAC-SHA256 signature
HMAC6 [48 bit value] [6 bytes] Specifies bits 224-271 of the HMAC-SHA256 signature
Frame ID | Prio [1] | Cmd [1] | HMAC6 [6]
0x00004711 | 0x04 | 0x09 | 0x1F1E1D1C1B1A

## Slide 19
CAN Rule Configuration – PREP_RULE10
Cmd [PREP_RULE10] [1 byte]
Specifies six bytes of the HMAC-SHA256 signature
HMAC7[48 bit value] [6 bytes] Specifies bits 272-319 of the HMAC-SHA256 signature
Frame ID | Prio [1] | Cmd [1] | HMAC7 [6]
0x00004711 | 0x04 | 0x10 | 0x252423222120

## Slide 20
CAN Rule Configuration – STORE_RULE
Cmd [STORE_RULE] [1 byte]
Stores the rule specified by PREP_RULE1 to PREP_RULE6
Seq [32bit value] [4 byte] Unique sequence number for this given Prio. Value must be greater than previously received value for the given Prio in order for the rule to be processed. Stops replay attacks.
Unused [2 bytes] Not used. Must be 0
Frame ID | Prio [1] | Cmd [1] | Seq[4] | Unused[2]
0x00004711 | 0x04 | 0x11 | 0x00000001 | 0x0000

## Slide 21
CAN Rule Configuration – Example
0x00004711 | 0x04 | 0x01 [PREP_RULE1] | Mask: 0x0000FFFF | XForm: 0x01 | Rsvd: 0x00
0x00004711 | 0x04 | 0x02 [PREP_RULE2] | Filter: 0x0000AAC1 | DtOper1: 0x0100
0x00004711 | 0x04 | 0x03 [PREP_RULE3] | DtOper2: 0x070605040302
0x00004711 | 0x04 | 0x04 [PREP_RULE4] | IDOper: 0xFFFF0000 | HMAC1: 0x0100
0x00004711 | 0x04 | 0x05 [PREP_RULE5] | HMAC2: 0x070605040302
0x00004711 | 0x04 | 0x06 [PREP_RULE6] | HMAC3: 0x0D0C0B0A0908
Frame ID | Prio | Cmd | Command Parameters
Prio | Mask | Filter | ID XForm | Data XForm | ID Operand | Data Operand
0x04 | 0x0000FFFFF | 0x0000AAC1 | SET | AND | 0xFFFF0000 | 0x0706050403020100
0x00004711 | 0x04 | 0x07 [PREP_RULE7] | HMAC4: 0x131211100F0E
0x00004711 | 0x04 | 0x08 [PREP_RULE8] | HMAC5: 0x191817161514
0x00004711 | 0x04 | 0x09 [PREP_RULE9] | HMAC6: 0x1F1E1D1C1B1A
0x00004711 | 0x04 | 0x10 [PREP_RULE10] | HMAC7: 0x252423222120
0x00004711 | 0x04 | 0x11 [STORE_RULE] | Seq: 0x00000001 | Unused: 0x0000

## Slide 22
Signature Payload used by HMAC-SHA256
0x00004711 | 0x04 | 0x01 [PREP_RULE1] | Mask: 0x0000FFFF | XForm: 0x01 | Rsvd: 0x00
0x00004711 | 0x04 | 0x02 [PREP_RULE2] | Filter: 0x0000AAC1 | DtOper1: 0x0100
0x00004711 | 0x04 | 0x03 [PREP_RULE3] | DtOper2: 0x070605040302
0x00004711 | 0x04 | 0x04 [PREP_RULE4] | IDOper: 0xFFFF0000 | HMAC1: 0x0100
0x00004711 | 0x04 | 0x05 [PREP_RULE5] | HMAC2: 0x070605040302
0x00004711 | 0x04 | 0x11 [STORE_RULE] | Seq: 0x00000001 | Unused: 0x0000
Frame ID | Prio | Cmd | Command Parameters
Prio | Mask | XForm | Rsvd | Filter | Data Operand | ID Operand | Sequence | Unused
0x04 | 0x0000FFFF | 0x01 | 0x00 | 0x0000AAC1 | 0x0706050403020100 | 0xFFFF0000 | 0x00000001 | 0x0000
Signature Payload string [25 bytes] (Color coded fields)
0x040000FFFF01000000AAC10706050403020100FFFF0000000000010000
…